## Slide 1
Wireless Networking
Lecture 9
Mobile IP

## Slide 2: References
Schiller, J.H. (2003), Mobile Communications, Second Chapter 8: Mobile Network Layer

## Slide 3: Objectives
Motivation and Requirements
Data Transfer using Tunnelling
Encapsulation
Optimisation of Packet Forwarding
Reverse Tunnelling
Mobile IP and IPv6
Problems with Mobile IP
Mobility in Cellular Networks

## Slide 4: Motivation
Routing
  based on IP destination address, network prefix (e.g. 129.13.42) determines physical subnet
  change of physical subnet implies change of IP address to have a topological correct address (standard IP) or needs special entries in the routing tables
Specific routes to end-systems?
  change of all routing table entries to forward packets to the right destination
  does not scale with the number of mobile hosts and frequent changes in the location, security problems

## Slide 5: Motivation
Changing the IP-address?
  adjust the host IP address depending on the current location
  almost impossible to find a mobile system, DNS updates take to long time
  TCP connections break, security problems

## Slide 6: Requirements for Mobile IPv4
Transparency
  mobile end-systems keep their IP address
  continuation of communication after interruption of link possible
  point of connection to the fixed network can be changed
Compatibility
  support of the same layer 2 protocols as IP
  no changes to current end-systems and routers required
  mobile end-systems can communicate with fixed systems

## Slide 7: Requirements for Mobile IPv4
Security
  authentication of all registration messages
Efficiency and scalability
  only little additional messages to the mobile system required (connection typically via a low bandwidth radio link)
  world-wide support of a large number of mobile systems in the whole Internet

## Slide 8: Terminology
Mobile Node (MN)
  system (node) that can change the point of connection to the network without changing its IP address
Home Agent (HA)
  system in the home network of the MN, typically a router
  registers the location of the MN, tunnels IP datagrams to the COA
Foreign Agent (FA)
  system in the current foreign network of the MN, typically a router
  forwards the tunneled datagrams to the MN, typically also the default router for the MN

## Slide 9: Terminology
Care-of Address (COA)
  address of the current tunnel end-point for the MN (at FA or MN)
  actual location of the MN from an IP point of view
  can be chosen, e.g., via DHCP
Correspondent Node (CN)
  communication partner

## Slide 10: Main Capabilities of Mobile IP
Discovery: A mobile node uses a discovery procedure to identify prospective home agents and foreign agents.
Registration: A mobile node uses an authenticated registration procedure to inform its home agent of its care-of address.
Tunneling: Tunneling is used to forward IP datagrams from a home address to a care-of address.

## Slide 11: Example Network
mobile end-system
Internet
router
router
router
end-system
FA
HA
MN
home network
foreign network
(physical home network
for the MN)
(current physical network for the MN)
CN

## Slide 12: Data transfer to the mobile system
Internet
sender
FA
HA
MN
home network
foreign
network
receiver
1
2
3
1. Sender sends to the IP address of MN,
HA intercepts packet (proxy ARP)
2. HA tunnels packet to COA, here FA,
by encapsulation
3. FA forwards the packet to the MN
CN

## Slide 13: Data transfer from the mobile system
Internet
receiver
FA
HA
MN
home network
foreign network
sender
1
1. Sender sends to the IP address of the receiver as usual, FA works as default router
CN

## Slide 14: Overview of Tunnelling
CN
router
HA
router
FA
Internet
router
1.
2.
3.
home
network
MN
foreign
network
4.
CN
router
HA
router
FA
Internet
router
home
network
MN
foreign
network
COA

## Slide 15: Encapsulation
original IP header
original data
new data
new IP header
outer header
inner header
original data

## Slide 16: Encapsulation
Encapsulation of one packet into another as payload
IP-in-IP-encapsulation (mandatory, RFC 2003)
  tunnel between HA and COA
Care-of address COA
IP address of HA
TTL
IP identification
IP-in-IP
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
IP address of MN
IP address of CN
TTL
IP identification
lay. 4 prot.
IP checksum
flags
fragment offset
length
DS (TOS)
ver.
IHL
TCP/UDP/ ... payload

## Slide 17: Optimisation of Packet Forwarding
Problem: Triangular Routing
  sender sends all packets via HA to MN
  higher latency and network load
“Solutions”
  sender learns the current location of MN
  direct tunneling to this location
  HA informs a sender about the location of MN
  big security problems!

## Slide 18: Optimisation of Packet Forwarding
Change of FA
  packets on-the-fly during the change can be lost
  new FA informs old FA to avoid packet loss, old FA now forwards remaining packets to new FA
  this information also enables the old FA to release resources for the MN

## Slide 19: Some reasons for Reverse Tunnelling
Firewalls: Reverse tunnel required to enable packets pass through firewall.
Multi-cast: Reverse tunnel needed for the MN to participate in a multicast group.
Time-to-live (TTL): Reverse tunnel is required that represents just one hop.

## Slide 20: Reverse Tunnelling
Internet
receiver
FA
HA
MN
home network
foreign network
sender
3
2
1
1. MN sends to FA
2. FA tunnels packets to HA
by encapsulation
3. HA forwards the packet to the
receiver (standard case)
CN

## Slide 21: Mobile IPv6
Mobile IPv6 provides mobility support for IPv6. It allows devices to keep the same internet address all over the world, and allows applications using that address to maintain transport and upper-layer connections when changing locations.
In Mobile IPv6, each mobile node is identified by two IP addresses: its home address and its care-of address. The home address is a permanent IP address that identifies the mobile node regardless of its location. The care-of address changes at each new point of attachment and provides information about the mobile node's current situation. When a mobile node arrives to a visited network, it must acquire a care-of address.

## Slide 22: Mobile IPv6
Mobile IP was developed for IPv4, but IPv6 simplifies the protocols
  security is integrated and not an add-on, authentication of registration is included
  COA can be assigned via auto-configuration (DHCPv6 is one candidate)
  MN can signal a sender directly the COA, sending via HA not needed in this case

## Slide 23: Mobile IPv6
  “soft” hand-over, i.e. without packet loss, between two networks is supported
    MN sends the new COA to its old router
    the old router encapsulates all incoming packets for the MN and forwards them to the new COA
    authentication is always granted

## Slide 24: Problems with Mobile IP
Security
  authentication with FA problematic, for the FA typically belongs to another organization
  no protocol for key management and key distribution has been standardized in the Internet
  patent and export restrictions
Firewalls
  typically mobile IP cannot be used together with firewalls, special set-ups are needed (such as reverse tunneling)
QoS
  tunneling makes it hard to give a flow of packets a special treatment needed for the QoS
Security, firewalls, QoS etc. are topics of research and discussions

## Slide 25: Mobility in Cellular Networks
correspondent
MSC
MSC
MSC
MSC
MSC
wired public telephone
network
different cellular networks,
operated by different providers

## Slide 26: Mobility in Cellular Networks
Home Network:
    Network of cellular provider you subscribe to (e.g., Sprint PCS, Verizon)
  home location register (HLR): database in home network containing permanent cell phone #, profile information (services, preferences, billing), information about current location (could be in another network)
Visited Network:
    Network in which mobile currently resides
  visitor location register (VLR): database with entry for each user currently in network
  could be home network

## Slide 27: Mobility in Cellular Networks
Public switched
telephone
network
mobile
user
home
Mobile
Switching
Center
HLR
home
network
visited
network
correspondent
Mobile
Switching
Center
VLR
1
call routed
to home network
2
home MSC consults HLR,
gets roaming number of
mobile in visited network
3
home MSC sets up 2nd leg of call
to MSC in visited network
4
MSC in visited network completes
call through base station to mobile